## Slide 1: Capacity Planning Break-Even Point Ardavan Asef-Vaziri Systems and Operations Management College of Business and Economics California State University, Northridge

## Slide 2
Capacity Planning: Break-Even Analysis
Operation costs are divided into 2 main groups:
  Fixed costs – Costs of Human and Capital Resources
  wages, depreciation, rent, property tax, property insurance.
  the total fixed cost is fixed throughout the year. No matter if we produce one unit or one million units. It does not depend on the production level.
  fixed cost per unit of production is variable.
Variable costs – Costs of Inputs
  raw material, packaging material, supplies, production water and power.
  The total variable costs depend on the volume of production. The higher the production level, the higher the total variable costs.
  variable cost per unit of production is fixed.

## Slide 3: Five Elements of the Process View
Outputs
Goods
Services
Human & Capital
Information
structure
Network of
Activities and Buffers
Inputs
(natural or processed resources, parts and components, energy, data, customers, cash, etc.)
Resources
Process
Management
Flow Unit
Variable
Fixed

## Slide 4
Total Fixed Cost and Fixed Cost per Unit of Product
Total fixed cost
(F)
Production volume (Q)
Fixed cost per unit of product
(F/Q)
Production volume (Q)

## Slide 5
Variable Cost per Unit and Total Variable Costs
Total Variable costs
(VQ)
Variable costs
Per unit of product
(V)
Production volume (Q)
Production volume (Q)

## Slide 6
Total Costs in $ (TC)
0
Volume of Production and Sales in units (Q)
Total variable cost (VQ)
Total Fixed cost (F)
Total cost = F+VQ
Total Costs TC = F+VQ

## Slide 7
Total Revenue
It is assumed that the price of the product is fixed,
and we sell whatever we produce.
Total sales revenue depends on the production level. The higher the production, the higher the total sales revenue.

## Slide 8
Total Costs or Revenue in $ (TC)
Volume of Production and Sales in units (Q)
Total Revenue (PQ)
Total cost = F+VQ
Loss
Profit
Break-Even Point
Break-Even Computations

## Slide 9
Example 1
$1000,000 total yearly fixed costs.
$200 per unit variable costs
$400 per unit sale price
TR = TC
400Q= 1000,000+200Q
(400-200)Q= 1000,000
Q= 5000
QBEP=5000
If our market research indicates that the present demand is > 5,000, then this manufacturing system is economically feasible.

## Slide 10
BEA for Multiple Alternatives
Break-even analysis for multiple alternatives:
Such an analysis is implemented to compare cases such as
In general, when we move from a simple technology to an advanced technology; F  V
A Simple technology
An Intermediate technology
An Advanced technology
General purpose machines
Multi-purpose machines
Special purpose machines
Low F high V
In between
High F Low V

## Slide 11
BEA for Multiple Alternatives
Job-Shop
Batch
Flow-Shop
Q1
Q2

## Slide 12
Example 2
Management should decide whether to make a part at house or outsource it. Outsource at $10 per unit.
To make it at house; two processes: Advanced and Intermediate
(1) At house with intermediate process Fixed Cost: $10,000/year Variable Cost: $8 per unit
(2) At house with advanced process. Fixed Cost: $34,000/year Variable Cost: $5 per unit
Prepare a table to summarize your recommendations.
Demand Recommendation
R ≤ ? ?
? ≤ R ≤ ? ?
? ≤ R ?

## Slide 13
Example 2. BEA for Multiple Alternatives
Outsource
Manufacture I
Manufacture II
Q1
Q2

## Slide 14
Example 2. Outsource vs. Manufacturing I
10Q
10,000+8Q
10000+8Q=10Q
2Q=10000
Q=5000
1000
2000
3000
4000
5000
6000
7000
8000
9000
10000
10000
20000
30000
40000
50000
60000
70000
80000
90000
100000

## Slide 15
Example 2. Manufacturing I vs. Manufacturing II
34,000+5Q
10,000+8Q
10000+8Q=34000+5Q
3Q=24000
Q=8000
1000
2000
3000
4000
5000
6000
7000
8000
9000
10000
10000
20000
30000
40000
50000
60000
70000
80000
90000
100000

## Slide 16
Example 2. Executive Summary
We summarize our recommendations as
Demand Recommendation
R ≤ 5000 Buy
5000 ≤ R ≤ 8000 Manufacture Alternative I
8000 ≤ R Manufacture Alternative II
On the boundary points, in practice, we need more information

## Slide 17
Three alternatives
1) Job-Shop
Total Fixed Cost F = $10,000,
Variable cost V = $10 per unit
2) Group-Shop
Total Fixed Cost F = $60,000,
Variable cost V = $5 per unit
3) Flow-Shop
Total Fixed Cost F = $150,000,
Variable cost V = $2 per unit
Example 3. BEA for Multiple Alternatives
Tell me what to do: In terms of the range of demand and the preferred choice…

## Slide 18
Example 3. BEA for Multiple Alternatives
Job-Shop
Group-Shop
Flow-Shop
Q1
Q2

## Slide 19
Example 3. BEA, Job-Shop vs. Batch Processing
Job-Shop
Group-Shop
Q1

## Slide 20
F1=10000 V1=10
F2=60000 V2=5
Q =
Example 3. BEA, Job-Shop vs. Batch Processing
Break-even of 1 and 2
F1+ V1 Q = F2+ V2 Q
10000+10Q = 60000 + 5Q

## Slide 21
Example 3. Batch Processing vs. Flow Shop
Group-Shop
Flow-Shop
Q2

## Slide 22
F2=60000 V2=5
F3=150000 V3=2
Q =
Example 3. Batch Processing vs. Flow Shop
Break-even of 2 and 3
F2+ V2 Q = F3+ V3 Q
60000 + 5Q = 150000+2Q

## Slide 23
Demand Recommended Alternative
D 10000 Job-Shop
10000 D 30000 Group-Shop
30000 D Flow-Shop
We also need to know Price and Revenue!
Suppose sales price is $8 per unit. Revise the table
Recommendations to Management and Marketing

## Slide 24
Alternative 1 has a variable cost of $10>$8 will never use it
Alternative 2 has a variable cost of $5<$8
Alternative 3 has a variable cost of $2<$8
As we saw before, Alternatives 2 and 3 break even at 30,000
If demand is greater than 30,000, we use alternative 3.
Now we can compute the break-even point of Alternative 2.
Can you analyze the situation before solving the problem?
If the break-even point for alternative 2 is X and is greater than 30,000, then we never use Alternative 2 since beyond a demand of 30,000, Alternative 3 is always preferred to Alternative 2.
D < X Do nothing
D> X Alternative 3
Lets see where is the BEP of alternative 2
F+VQ = PQ
60,000+5Q=8Q  Q= 20,000.
Recommendations to Management and Marketing

## Slide 25
D < 20,000 Do nothing
20,000 < D < 30,000 Alternative 2
30,000 < D Alternative 3
If sales price was $6.5 instead of $8, then
F+VQ = PQ
60,000+5Q=6.5Q
Q= 40,000.
But for Q> 30,000 you never use Alternative 2, but Alternative 3
Where Alternative 3 breaks even?
150000+2Q = 6.5Q
150000 = 4.5 Q  Q = 33333
D 33333 Do nothing
D ≥ 30,000 Alternative 3
Recommendations to Management and Marketing

## Slide 26
Example 4. BEP for the Three Global Locations
You’re considering a new manufacturing plant in the sites at the suburb of one of the three candidate locations of:
Bristol (England), Taranto (Italy), or Essen (Germany).
Total Fixed costs (costs of human and capital resources) per year and variable costs (costs of inputs) per case of product is given below
Bristol (England) F = $300000, V = $18
Essen (Germany): F = $600000, V = $12
Taranto (Italy): F = $900000, V = $9

## Slide 27
Example 3. BEA for Multiple Alternatives
Bristol
Essen
Taranto
Q1
Q2

## Slide 28
Example 3. BEA for Multiple Alternatives
Bristol
Essen
Taranto
Q1
Q2

## Slide 29
Example 4. BEP for the Three Global Locations
1. At what level of demand a site at Bristol suburb is preferred?
Bristol Total Costs = 300000+18Q
Essen Total Costs = 600000+12Q
300000+18Q = 600000+12Q
6Q = 300,000
Q = 50,000
2. At what level of demand is a site at Essen suburb preferred?
Essen Total Costs = 600000+12Q
Taranto Total Costs = 900000+9Q
600000+12Q = 900000+9Q
3Q = 300,000
Q = 100,0000
Essen is preferred for 100,000≥ Q ≥ 50,000

## Slide 30
Example 3. BEA for Multiple Alternatives
Bristol
Essen
Taranto
50000
100000

## Slide 31
Example 4. BEP for the Three Global Locations
3. At what level of demand a site at Taranto suburb is preferred?
More than 100,000
4. Suppose sales price is equal to the average of the variable costs at Bristol and Essen. At what level of demand is a site at Bristol suburb preferred?
Never
6. Given the same assumption as (4). At what level of demand a site at Essen suburb is preferred?
P = (18+12)/2 = 15
Total Essen cost = 600,000 + 12Q
PQ = F + VQ
15Q = 600,000 + 12Q
3Q = 600,000
Q = 200,000
Never. Why???

## Slide 32
Example 5. BEP for the Three Global Locations
Why
At Q = 100,000 Taranto dominates Essen
5. Given the same assumption as (4). At what level of demand is a site at Taranto suburb preferred?
P = (18+12)/2 = 15
Taranto Total cost = 900,000 + 9Q
PQ = F + VQ
15Q = 900,000 + 9Q
6Q = 900,000
Q = 150,000
P =15
D ≤ 150000 No Where
D ≥ 150,000 Taranto

## Slide 33
Example 5. BEP for the Three Global Locations
7. Suppose sales price is $20. At what level of demand a site at Essen suburb is preferred?
Essen Total cost = 600,000 + 12Q
20Q = 600,000+12Q
Q = 75000
From 75000 to ??
At what level of demand a site at Essen is preferred?
At 100,000 Essen and Taranto Break Even – After that Taranto denominates
From 75,000 to 100,000
P= 20
75,000 ≤ D ≤ 100000 Essen
D ≥ 100,000 Taranto

## Slide 34: Financial Throughput and Fixed Operating Costs
We define financial throughput as the rate at which the enterprise generates money. By selling one unit of product we generate P dollars, at the same time we incur V dollars pure variable cost. Pure variable cost is the cost directly related to the production of one additional unit - such as raw material. It does not include sunk costs such as salary, rent, and depreciation. Since we produce and sell Q units per unit of time. The financial throughput is Q(P-V).
Fixed Operating Expenses (F) include all costs not directly related to production of one additional unit. That includes costs such as human and capital resources.
Throughput Profit Multiplier = % Changes in Profit divided by % Changes in Throughput
1% change in the throughput leads to TPM% change in the profit

## Slide 35: Financial Throughput and Fixed Operating Costs
Suppose fixed cost F = $180,000 per month. Sales price per unit P = 22, and variable cost per unit V = 2. In July, the process throughput was 10,000 units. A process improvement increased throughput in August by 2% to 10,200 units without any increase in the fixed cost. Compute throughput profit multiplier.
July: Financial Throughput = 10000(22-2) = 200000
Fixed cost F = 180,000
Profit = 200000-180000 = $20,000
In August throughput increased by 2% to 10200
August: Financial Throughput of the additional 200 units = 200(22-2) = 4,000
We have already covered our fixed costs, the $4000 directly goes to profit.

## Slide 36: Throughput Profit Multiplier (TPM)
% Change in Throughput = 2%
% change in profit = 4000/20000 = 20%
Throughput Profit Multiplier (TPM) = 20%/2% = 10
1% throughput improvement  10% profit improvement

## Slide 37: A Viable Vision – Eliyahu Goldratt
A Viable Vision (Goldratt): What if we decide to have todays total revenue as tomorrows total profit.
In our example, Financial Throughput in July was Q1(P-V) = 10,000(22-2). In order to have your profit equal this amount we need to produce Q2 units such that:
Q2(P-V) – F = Q1(P)
Q2(20) -180,000 = 10,000(22)
Q2(20) = 40,000
Q2 = 20,000
In order to have your todays total revenue as tomorrows total profit. We only need to double our throughput. Our sales, our current revenue becomes our tomorrows profit.

## Slide 38
A manager has the option of purchasing 1, 2 or 3 machines.
The capacity of each machine is 300 units.
Fixed costs are as follows:
Number of Machines Fixed cost Total Capacity
1 $9,600 1-300
2 $15,000 301-600
3 $20,000 601-900
Variable cost is $10 per unit, and the sales price of product is $40 per unit.
Tell management what to do!
Example 5

## Slide 39
Example 5. BEP Recommendations
Prepare an executive summary similar the following:
R<= ?  ?
?<R<=?  ?
R>?  ?
Now it is up to the Marketing Department to provide an Executive Summary regarding the demand.

## Slide 40
BEP: One Machine
100
200
300
400
500
600
700
800
900
1000
5000
10000
15000
20000
25000
30000
35000
40000
9600+10Q
40Q
320
9600 + 10Q = 40Q
9600= 30Q
The beak-even point for 1 machine is 320
But one machine can not produce more than 300
Demand <= 300  No Production
Otherwise  Consider two machines

## Slide 41
BEP: Two Machine
100
200
300
400
500
600
700
800
900
1000
5000
10000
15000
20000
25000
30000
35000
40000
15000+10Q
40Q
500
15000 + 10Q = 40Q
15000= 30Q
The beak-even point for 2 machine is 500
Demand <= 500  No Production
Otherwise  Two machines and consider 3 machines

## Slide 42
BEP: Three Machine
100
200
300
400
500
600
700
800
900
1000
5000
10000
15000
20000
25000
30000
35000
40000
20000+10Q
40Q
667
20000 + 10Q = 40Q
20000= 30Q
The beak-even point for 3 machine is 667
Demand <= 667  Produce up to 600 using 2 machine
Otherwise  3 machines

## Slide 43
BEP for the Three Alternatives and Recommendations
Prepare an executive summary similar the following:
R<= 500  Do nothing
500 <R<=667  Buy two machines and produce 500< Q<= 600
Q>667  Buy three machines and produce 667<R<=900
Now it is up to the Marketing Department to provide an Executive Summary regarding the demand.
Please Think again!.
We have made a mistake.

## Slide 44
BEP: Two Machine- Revisited
100
200
300
400
500
600
700
800
900
1000
5000
10000
15000
20000
25000
30000
35000
40000
15000+10Q
40Q
600
TC = 15000 + 10(600)
TC = 21000
TR = 40(600) = 24000
Profit = 24000-21000 = 3000
}
You do not switch to 3 machines unless you make 3000 profit

## Slide 45
From Wrong to Right Recommendations
Q<= 500  Do-Nothing
500<Q<=667  Buy two machines and produce 500<Q<= 600
Q>667  Buy three machines and produce 667<Q<=900
20000 + 10Q = 40Q
20000= 30Q
Q = 667
20000 + 10Q +3000= 40Q
23000= 30Q
Q = 767
At Q = 667 you make 0 profit with 3 machines

## Slide 46
Executive Summary
Q<= 500  Do-Nothing
500<Q<=767  Buy two machines and produce 500<Q<= 600
Q>767  Buy three machines and produce 767<Q<=900
Now it is to Marketing Department to provide executive summary regarding the demand

## Slide 47
You are the production manager and are given the option to purchase either 1, 2 or 3 machines. Each machine has a capacity of 500 units. Fixed costs are as follows:
Number of Machines Fixed cost Total Capacity
1 $19,200 1- 500
2 $30,000 501-1000
3 $40,000 1001-1500
Variable cost is $35 per unit, and the sales price of product is $69 per unit.
Determine the best option!
Example 5- At Your Own Will

## Slide 48
BEP for the Three Alternatives and Recommendations
Prepare an executive summary similar the following:
R<= ?  ?
?<R<=?  ?
R>?  ?

## Slide 49
Variable Cost Per Unit is Not Fixed – Diminishing Marginal Return
Output
Input
Variable costs
Per unit of product
(V)
Production volume
(Q)

## Slide 50: Economy of Scale- Dis-economy of Scale
LO4
Long-Run
ATC
Average Total Costs
ATC-1
ATC-2
ATC-3
ATC-4
ATC-5
Output
7-50

## Slide 51: Note on the Basic MEP Model
LO2
Increasing
Marginal
Returns
Diminishing
Marginal
Returns
Negative
Marginal
Returns
1
2
3
4
5
6
7
8
9
0
10
20
30
Total Production
1
2
3
4
5
6
7
8
9
20
10
Marginal and Average Production
7-51
MP
AP
TP

## Slide 52: A Viable Vision – Eliyahu Goldrat
Economies of scale
  Labor specialization
  Managerial specialization
  Efficient capital
  -------------
Diseconomies of scale
  Control and coordination problems
  Communication problems
  Worker alienation
  Shirking
  Dinosaur Effect

## Slide 53
BEA Simulation

## Slide 54
Back to Example1 - Simulation
$1000,000 average total yearly fixed costs ($800,000-$1,200,000).
$200 average per unit variable costs ($180-$220).
$400 average per unit sale price ($350-$450)
Sales 4000-6000
.