## Slide 1: Job Shop, Flow Shop, and Group Shop

## Slide 2: Low Cost vs High Flexibility
Process Cost: the total cost of producing and delivering outputs. Remove NVA activities and buffers (BPR).
  Division of labor. Break the whole job into small pieces. Allocation of appropriate recourses. Lower than appropriate is cheap, but quality goes down. Higher than appropriate, adds to the costs.
  High standardization. Low variations
  High Utilization.
Process Flexibility: the ability to produce and deliver a variety of products at high and low production volumes.
  Cross trained workers
  General purpose equipment + short set-up time
  Delayed differentiation
  Job-Shop layout or U-shaped layout
  Small batch size.

## Slide 3: Operations Management Defined
If I am forced to define Operations Management in one line  Create a Smooth Flow. Smooth flow means (i) low cost production cost because flow units do not have time to collect cost, (ii) high quality because as soon as quality problem is observed, we must stop production, i.e., no smooth flow, and (iii) system is flexible because we do not have too much inventory and can easily respond to technological advances and changes in customer preferences and switch to new products.
If I am forced to provide another short definition for Operations Management  OM is the concepts, ideas, methods, models, and the whole body of knowledge to understand trade-offs.

## Slide 4: Operations Management Defined
If I am forced to provide still another short definition for Operations Management  OM is the concepts, ideas, methods, models, and the whole body of knowledge to remove variability.
OM is the concepts, ideas, methodologies, models, and the whole body of knowledge to create a smooth flow, understand trade-off, and remove variability, and create strategic fit between product attributes and process competencies.

## Slide 5: Process Architecture: Job Shop vs. Flow Shop
Job Shop- Functional layout or Process Layout: similar resources in the same department. Ex. all press machines are located in stamping department. Ex. Bakeries, law firms, emergency rooms, repair shops.
Flow Shop- Product layout or line layout: Resources are arranged according to the sequence of the operations. Usually requires duplication ( and investment) of a resource pool; dedication of resources. Discrete flow shop; assembly line, Continuous flow shop; beverage.
Group Shop – Group Technology or Cellular Layout: Something between job shop and flow shop. Parts and products are grouped in families, a pseudo flow shop is arranged for each family.
Batch Processing – A combination of job shop and flow shop for batches.

## Slide 6: Facility Layout : Job Shop
A
C
B
D
Part1
Part2
Part3
Product1
Product2
Part4

## Slide 7: Facility Layout : Flow Shop
Part1
A
C
D
Part2
B
C
D
Part3
A
B
Product1
Product2
Part4

## Slide 8: Job Shop vs. Flow Shop
Job Shop
  Low volume, high variety products, customization
  Flexible capital resources (general purpose equipment)
  Skilled human resources, cross trained workers
  Complicated work flows (Spaghetti style material flow)
  Slow material handling over long distances
  Large volume of inventories
  Long flow time (both in material handling and processes)
  High variable cost but low initial investment
  Difficult product tracing
Flow Shop
  Everything opposite of job shop.

## Slide 9: Facility Layout : Group Shop
Part1
A
Part2
B
C
D
Part3
B
Product1
Product2
Part4
Most processes fall somewhere on the continuum between Job Shop and Flow Shop; batch processing.

## Slide 10: A Job Shop
Drilling
D
D
D
D
Grinding
G
G
G
G
G
G
Milling
M
M
M
M
M
M
Assembly
A
A
A
A
Lathing
Receiving and shipping
L
L
L
L
L
L
L
L

## Slide 11: A Group Shop Very Close to Flow Shop
L
M
G
G
Assembly area
A
A
L
M
D
L
L
M
Shipping
D
Receiving
G

## Slide 12: Strategic Fit: The Product-Process Matrix
The product-process matrix is a strategic fit tool. It focuses on the match between product attributes – defined by the market segment and reflected in the customer value proposition – and process capabilities to deliver value.
It verifies alignment, often by comparing the degree of variety in the value proposition with the degree of flexibility in the process. This combination is then represented by a covered area in the matrix where the distance to the diagonal represents the degree of misalignment.

## Slide 13: Matching Process Choice with Strategy: Product-Process Matrix For Discrete Floew
FLOW SHOP
Product Line
Process Capability
Flexibility
Product Attribute
Variety
Low
High
Low
High
Jumbled Flow
General Purpose CR
Skilled HR
FC ↓, VC↑
Well Designed Flow Lines
Special Purpose CR
Low Skill HR
VC ↓, FC↑
Variety ↓
Volume ↑
Variety ↑
Volume ↓
GROUP SHOP
Product Families
JOB SHOP
Process Layout
Opportunity Cost

## Slide 14: Matching Process Choice with Strategy: Product-Process Matrix For Discrete Floew
Process Capability
Flexibility
Product Attribute
Variety
Low
High
Low
High
Jumbled Flow
General Purpose CR
Skilled HR
FC ↓, VC↑
Well Designed Flow Lines
Special Purpose CR
Low Skill HR
VC ↓, FC↑
Variety ↓
Volume ↑
Variety ↑
Volume ↓
JOB SHOP
Process Layout
GROUP SHOP
Product Families
FLOW SHOP
Product Line
Out of Pocket Cost

## Slide 15: The Product-Process Matrix
Positions outside the diagonal signal misalignment. Three star chefs who serve simple meals (burritos and tacos) with their highly flexible job shop process incur high opportunity costs. Substantial savings would result from changing resources (including chefs) and streamlining the process into a flow shop.
Asking Chipotle's to change its menu daily would require high changeover costs. Asking it to deliver a three-star dining experience is virtually impossible.
A similar graph can be prepared to show the relationship between Product Attribute of Variety and Process Capability of Cost, or Process Capability of Response Time, but not for Quality.

## Slide 16: Facility Layout : Job Shop
A
C
B
D
Product 1
Output
Input
Product 2

## Slide 17: Facility Layout : Flow Shop
Output
Input
A
C
B
D
B
A
Product 1
Product 2