## Slide 1: Three Key Process Measures: Flow Rate
Process
  Ro(t)
Ri,2(t)
  Ri,1(t)
Ri,1(t): Instantaneous inflow rate at entry 1
Ri,2(t): Instantaneous inflow rate at entry 2
Ro(t): Instantaneous outflow rate at the exit point
ΔR(t) = Ri,1(t) + Ri,2(t) - Ro(t)
Notes: Instantaneous flow rate is represented by R(t)
As you could see in the slide (look at diagram)

## Slide 2: MBPF Inc: Manufacturing Prefabricated Garages
Notes: As you remember from the text book, MBPF Inc manufactures garages. Production and Demand for these garages vary from week-to-week.
We regard the finished goods inventory warehouse as the PROCESS and each garage as a FLOW UNIT. The production rate is the inflow and the demand (sales) is the outflow rate.

## Slide 3: Three Key Process Measures: Vancouver Airport
Flow unit = Passenger
Flow time = Total time spent by a passenger within security
process boundaries
Flow rate = the number of passengers leaving the checkpoint
Inventory = the number of passengers within process
boundaries at time t
  When Ri(t) > Ro(t)  I(t) increases
Each flight has 200 passengers.
If Ri(t) is 15 passengers/min, since Ro(t) can not exceed 12 passengers/min, then inventory increases.
Notes: Inventory is the total # of flow unis present within the process boundaries.
Inventory is linked to the flow rate by… (look at slide)
The total # of flow units present within the process boundaries at time t is denoted as I(t)
Note the case..

## Slide 4: Vancouver International Airport
Three flights at the start of each hour. The first flight is at 10 am.
50% of passengers arrive over a 20-minute time interval, 50 to 30
minutes before departure.
For all three flights 0.5(200)(3) = 300 passengers will arrive
uniformly between 9:10 - 9:30. Inflow rate = 300/20 = 15 passengers
per minute.
The remaining passengers arrive in a 40 minutes time interval either
80 to 50 minutes or 30 to 20 minutes before departure.
Therefore, between 8:40 - 9:10 and between 9:30 - 9:40 the inflow
rate is 300/40 = 7.5 passengers per minute.
Notes: As you remember, a process transforms units through activities and buffers until the creation of an output.
Flow time is the total time that unit spends within the process boundaries.
As a measure of process performance, flow time indicates the time needed to convert inputs into outputs and includes any time spent waiting fro processing activities.

## Slide 5: Inventory Build up Diagram for Vancouver Airport Security Checkpoint
0
Ri=15/min
Ro=12/min
Ri =Ro = 7.5/min
8:40
9:00
9:20
9:40
10:00
Ri < Ro =7.5/min
∆R=0/min
700
600
500
300
400
200
100
Cumulative in and outflow (passengers)
Time
∆R=3/min
Imax = 3(20)=60
∆R=-4.5/min
Tdeplete = 60/4.5 = 13.33 min
∆R=0/min
Notes: This shows us an inventory buildup diagram that together with the associated cumulative number of passengers arriving and departing from the check point.
By 910 the inflow is at 15/min and the output is still at 12/min so the buildup starts to grow. And it keeps growing because the when it starts to level off for the 10am flight at 940, the 11am passengers starts to grow. And the cycle continues.
THIS IS THE REASON WHY THERE IS A NEED TO STAGGER FLIGHTS.

## Slide 6: Average Inventory in a Stable Process
8:40-9:10: Ri = Ro
I1 = 0
9:10-9:30: Ri = 15, Ro =12
IMax = 3(20) = 60
Inventory is then depleted
at rate of (12-7.5) = 4.5
60/4.5 = 13.33
9:30 + 13.33 = 9:43
8:40
9:10
9:43
10:00
33 minutes
ΔR=0/min
ΔR= - 4.5/min
ΔR=3/min
ΔR=0/min
9:10-9:43: Average inventory = I2 = 60/2 = 30 passengers
Cycle repeats itself every hour,
I2=30 during 33 minutes and I1=0 during 27 minutes

## Slide 7: Average Inventory in a Stable Process
Cycle repeats itself every hour,
:10
:43
:00
:10
:43
:00
I2=30 during 33 minutes and I1=0 during 27 minutes
:10
:43
:00
:10
:43
:00
If you also want to take into account 8:40 to 9:00, and if the last three flights are at 10 p.m., then
I = (12 ×17.5 +0.33 ×0)/12.33 = 17.03

## Slide 8: A Stable Process
In a Stable Process
  Average outflow capacity must be greater than average inflow rate, while average inventory is not zero.
  Average inflow rate is the same as average outflow rate.
  Throughput (R) is the average flow rate
  Ideally, R should be equal to the customer demand.
Average inflow rate
is 600 passengers/hr,
or 10 passengers/min
Scanner can handle 12 passengers per minute
It can easily handle inflow
Is the Security Checkpoint a stable Process?

## Slide 9: Re-Scheduling the Flight: 0, 20, and 40 Minutes After Hour
If flight departures are staggered, the peaks and valleys in arrival rates for different flights cancel each other out as illustrated in this table
Inflow Rates with Staggered Departures for Vancouver Airport Security Checkpoint
Notes: Here is a table illustrating what happens if the flights are staggered. The shaded spaces correspond to the passenger arrivals for a particular flight.
By spreading out the flights, it will give you a constant arrival rate of 600 passengers per hour (10/min) at any point during the day.
Since this is below the process capacity of 12 passengers per minute, it would keep the build up rate at 0 and THERE WOULD BE NOBODY IN LINE.
WITH THAT, I WOULD LIKE TO TURN IT OVER TO ____________

## Slide 10
Orange Juice Inc. produces and markets fruit juice. During the orange harvest season, trucks bring oranges from the fields to the processing plant during a workday that runs from 7 a.m. to 6 p.m. On peak days, approximately 10,000 kilograms or oranges are trucked in per hour. Trucks dump their contents in a holding bin with a storage capacity of 6,000 kilograms. When the bin is full, incoming trucks must wait until it has sufficient available space. A conveyor moves oranges from the bins to the processing plant. The plant is configured to deal with an average harvesting day, and maximum throughput (flow rate) is 8,000 kilograms per hour.
Assuming that oranges arrive continuously over time, construct an inventory buildup diagram for Orange Juice Inc. In order to process all the oranges delivered during the day, how long must the plant operate on peak days? (Assume, too, that because Orange Juice Inc. makes fresh juice, it cannot store oranges.) Assuming, finally, that each truck holds about 1,000 kilograms of oranges, at what point during the day must a truck first wait before unloading into the storage bin? What is the maximum amount of time that a truck must wait? How long will trucks wait on average? Among trucks that do wait, how long is the average wait?
Problem 3.7, MBPF

## Slide 11: Directions
o) Assume a truck as your flow unit.
a) How long must the plant operate on peak days?
b) At what point during the day must a truck first wait before unloading into the storage bin?
c) What is the maximum amount of time that a truck must wait?
d) Among trucks that wait, how long is the average wait?
e) How long a truck wait on the average?