## Slide 1: Problem 1: M/M/1 Performance Evaluation
The arrival rate to a store is 6 customers per hour and follows Poisson distribution. The service time is 5 min per customer and follows exponential distribution.
a) Compute Processing time (How long does a customer stay with the cashier?)
Tp = 5 min.
b) On average how many customers are with cashier?
R= 6/ hr
Rp=1/Tp = 1/5 per min. or 60(1/5) = 12/hr
U= 6/12 = 0.5  Ip = 0.5
Alternatively;
RTp = Ip =
6(5/60) = 0.5
=(6/60)5 = 0.5

## Slide 2: Problem 1: M/M/1 Performance Evaluation
c) On average how many customers in the waiting line?
Where there is only one server, and both arrival rate and processing rate follow Poisson Process (that is the same as when interarrival time and processing time follow exponential distribution). Then the Ii formula is simplified to
Ii = 0.5 flow units (customers).

## Slide 3: Problem 1: M/M/1 Performance Evaluation
Ti =?
RTi =Ii
6Ti =0.5
Ti =0.5/6 hr
Ti =5 min
d) How long does a customer stay in the waiting line?
e) On average how many customers are in the system? I = ?
I = Ii+Ip  I =
f) On average how long does a customer stay in the system?
T = Ti+Tp  T =
0.5 +0.5 =1
5 + 5 =10
Alternatively RT=I
6T=1 1/6 hr or 10 min

## Slide 4: Problem 1: M/M/1 Performance Evaluation
g) What if the arrival rate is 11 per hour? Processing rate is still Rp=12.
U = R/Rp = 11/12
RTi = Ii
11Ti = 10.08
Ti = 10.08/11
Ti = 0.91667 hour
Ti = 0.91667(60) = 55 minutes
Compute the 6-variables for U=0.5 to U =0.99

## Slide 5: M/M/1 Performance Evaluation
As the utilization rate increases to 1 (100%) the number of customers in line (system) and the waiting time in line (in system) is increasing exponentially.

## Slide 6: M/M/1 Performance Evaluation

## Slide 7: Problem 2: M/M/1 Performance Evaluation
Case 1. An airport runway for arrivals only. Arriving aircraft join a single line for the runway. Exponentially distributed service time with a rate 25 arrivals /hour. Poisson arrivals with a rate 18 / hour. Compute Tp, Ip, Ii, Ti, I, and T.
R= 18 / hr
Rp=25/hr
U= 18/25 = 0.72
Ip = 0.72
Tp = 25 per 1 hours, how long for 1  Tp=1/25 hr or 60(1/25)  Tp= 2.4 min
Since there is only one server and Poisson processes in both arrival and service

## Slide 8: Problem 2: M/M/1 Performance Evaluation
Ti =?
RTi =Ii
18Ti =1.851429
Ti =1.851429/18
Ti =0.102857 hr or 6.171429
T= Ti+Tp = 8.57
I =Ii + Ip = 2.57

## Slide 9: Problem 2: M/M/1 Performance Evaluation
Case 2. Now suppose we are in holidays and the arrival rate increases to 22 arrivals/hour.
R= 21 / hr, Rp=25/hr  U= 21/25 = 0.84
Case 3. Now suppose we have a bad weather and the service rate decreases 22 landing /hour.
R= 21 / hr, Rp=22/hr  U= 21/22 = 0.95

## Slide 10: Problem 2: M/M/1 Performance Evaluation
Case 4. Now suppose we open a second runway. R=21, Rp=2*25/hr  U= 21/50 = 0.42

## Slide 11: Problem 3: M/G/c
An store on average has 10 customers /hr for the checkout line. The inter-arrival time follows the exponential distribution. The store has two cashiers. The service time for checkout follows a normal distribution with mean equal to 5 min and a standard deviation of 1 min.
Arrival rate: R = 10 per hour.
Number of servers: c =2.
Rp = c/Tp = 2/5 per min or 24 per hour.
U= R/Rp = 10/24 = 0.42
Average service time: Tp = 5 min
Standard deviation of service time: Sp = 1 min
Coefficient of variation for service time: Cp = Sp /Tp = 1/5 =0.2
Average inter-arrival time: Ta = 1/R = 1/10 hr = 6 min
Inter-arrival time is exponential  Ca = Sa/Ta = 1: Sa =Ta

## Slide 12: M/G/2 Example
a) On average how many customers are in the waiting line?
b) How long does a customer stay in the line?
RTi = Ii
10Ti = 0.11
Ti = 0.011 hour  Ti = 0.011(60) = 0.7 minute
c) How long does a customer stay in the processors (with the servers)?
Average service time: Tp = 5 min

## Slide 13: M/G/2 Example
d) On average how many customers are with the servers ?
RTp = Ip = (5/60)(10) = 0.84
Ip = cU = 2(0.42) = 0.84
e) On average how many customers are in the system?
I = ?
I = Ii+Ip
I = 0.11+0.84 = 0.95
f) On average how long does a customer stay in the system?
T= ?
T = Ti+Tp
T= 0.7+5 = 5.7 minutes

## Slide 14: Comment on General Formula
Approximation formula gives exact answers for M/M/1 system.
Approximation formula provide good approximations for M/M/2 system.

## Slide 15: Problem 4: M/M/c Example
A call center has 11 operators. The arrival rate of calls is 200 calls per hour. Each of the operators can serve 20 customers per hour. Assume inter-arrival time and processing time follow Poisson and Exponential, respectively. What is the average waiting time (time before a customer’s call is answered)?
U = 200/220 = 0.91, Ca = 1, Cp = 1
RTi = Ii
200Ti = 6.89
Ti = 0.0345 hour  Ti = 0.0345(60) = 2.1 min

## Slide 16: Problem 5: M/D/c Example
Suppose the service time is a constant
What is the answer to the previous question?
  In this case
RTi = Ii
200Ti = 3.45
Ti = 0.017 hour  Ti = 0.017(60) = 1.03 min

## Slide 17: Problem 1: M/M/1 Performance Evaluation
The arrival rate to a store is 6 customers per hour and follows Poisson distribution. The service time is 5 min per customer and follows exponential distribution.

## Slide 18: Additional Problems

## Slide 19: Problem A1
Students arrive at the Administrative Services Office on the average of one every 15 minutes, and their request take on average 10 minutes to be processed. The service counter clerk works 8 hours per day and is staffed by only 1 clerk, Judy Gumshoe. Assume Poisson arrivals and exponential service times.
M/M/1 Queuing System
R = 4 customers/hour, Poisson (Ca =1)
Rp = 6 customers/hour, Exponential (Cp =1)
a) What percentage of time is Judy idle?
b) How much time, on average, does a student spend waiting in line?

## Slide 20: Problem A1; M/M/1
a) What percentage of time is Judy idle?
U = R/Rp = 4/6 = 66.67% of time she is busy
1- U = 33.33% of time idle
b) How much time, on average, does a student spend waiting in line?
Ti R = Ii  Ti = Ii/R  1.33/4 = 0.33 hours
= 0.33 hours or 20 minutes

## Slide 21: Problem A2
You are working at a bank and doing resource requirements planning. You think that there should be six tellers working in the bank. Tellers take fifteen minutes per customer with a standard deviation of five minutes. On average one customer arrives in every three minutes according to an exponential distribution.
a) On average how many customers would be waiting in line?
b) On average how long would a customer spend in the bank?

## Slide 22
c = 6, R = 20, Rp = c/Tp = 6/15 /min, 60(6/15) = 24 /hr
U = R/Rp = 20/24 = 0.83
Ca = 1, Cp = 5/15 = 0.33
a) On average how many customers are in line?
b) On average how long would a customer spend in the bank?
Ti = Ii/R  1.62/20 = 0.081 hours, or 4.86 minutes
Tp = 15 minutes
T = Ti+Tp = 4.86+15 = 19.86 minutes
Problem A2; M/G/c

## Slide 23
Consider a call center with 8 agents. Past data has shown that the mean time between customer arrivals is 1 minute, and has a standard deviation of 1/2 minute. The amount of time in minutes the past 10 callers have spent talking to an agent is as follows: 4.1, 6.2, 5.5, 3.5, 3.2, 7.3, 8.4, 6.3, 2.6, 4.9.
a) What is the coefficient of variation for the inter-arrival times?
b) What is the mean time a caller spends talking to an agent?
c) What is the standard deviation of the time a caller spends talking to an agent?
d) What is the coefficient of variation for the times a caller spends talking to an agent?
e) What is the expected number of callers on hold, waiting to talk to an agent?
Problem

## Slide 24
a) What is the coefficient of variation for the inter-arrival times?
Ca = Sa/Ta = 0.5/1 = 0.5
b) What is the mean time a caller spends talking to an agent?
= average (4.1, 6.2, 5.5, 3.5, 3.2, 7.3, 8.4, 6.3, 2.6, 4.9) = 5.2 minutes.
c) What is the standard deviation of the time a caller spends talking to an agent?
  = stdev(4.1, 6.2, 5.5, 3.5, 3.2, 7.3, 8.4, 6.3, 2.6, 4.9) =1.88 minutes
Problem A3; G/G/1

## Slide 25
d) What is the coefficient of variation for the times a caller spends talking to an agent?
(standard deviation)/mean = 1.88/5.2 = 0.36
e) What is the expected number of callers on hold, waiting to talk to an agent?
R= 1 per minute, c = 8, processing rate for one agent is = 1/5.2. For c=8 agents, Rp = 8/5.2 = 1.54 /min
U = R/Rp= 1/(1.54) = 0.65
Problem A3

## Slide 26
f) What is the expected number of callers either on hold or talking to an agent?
I = Ii + Ip= 0.09 + 0.65(8) =5.29
g) What is the expected amount of time a caller must wait to talk to an agent?
RTi = Ii  Ti = 0.09/1 = 0.09 minutes
h) What is the expected amount of time between when a caller first arrives to the system, and when that caller finishes talking to an agent?
T = I/R = 5.29/1 = 5.29 minutes
Alternatively; T= Ti+Tp = 0.09+5.2 = 5.29
Problem A3

## Slide 27
Wells Fargo operates one ATM machine in a certain Trader Joe’s. There is on average 8 customers that use the ATM every hour, and each customer spends on average 6 minutes at the ATM. Assume customer arrivals follow a Poisson process, and the amount of time each customer spends at the ATM follows an exponential distribution.
Problem A4
a) What is the percentage of time the ATM is in use?
R = 8 per hour, Rp = 10 per hour
U = 8/10 = 0.8 =80%

## Slide 28
b) On average, how many customers are there in line waiting to use the ATM?
Problem A4 ; M/M/1
c) Suppose that the number of customers in line waiting to use the ATM is 3. (This may or may not be the answer you found in part b). All information remains as originally stated. What is the average time a customer must wait to use the ATM? State your answer in minutes.
TiR = Ii  Ti = 3/8 hr Ti = 3/8 (60) = 22.5 minutes

## Slide 29
The Matador housing office has one customer representative for walk-in students. The arrival rate is 10 customers per hour and the average service time is 5 minutes. Both inter-arrival time and service time follow exponential distributions.
a) What is the average waiting time in line?
R = 10 /hr, Rp = 12 /hr, U = 10/12= 0.83
Ti = Ii/R = 4.17/10 = 0.42 hr
Problem A4

## Slide 30
The Monterey post station has 7 tellers from Monday to Saturday. Customers arrive to the station following a Poisson process with a rate of 36 customers per hour. The service time is exponentially distributed with mean 10 minutes.
a) What is the utilization rate of the tellers?
R = 36, Rp = 7/10=0.7 /min or 42 /hr
U = R/Rp= 36/42 = 6/7 = 85.7%
b) What is the average number of customers waiting in line?
Problem A5

## Slide 31
On Sunday, instead of tellers, the post station only opens 3 auto-mail machines to provide automatic service. Each machine can weight the different size of packages, print self-adhesive labels and accept payments. Arrival is Poisson with rate 20 customers per hour. The service time has an average of 7 minutes and standard deviation of 5.2 minutes.
c) What is the mean service time?
Tp = 7 min
d) What is the coefficient of variation of service time?
Cp = 5.2 / 7 = 0.74
Problem A5

## Slide 32
e) What is the utilization rate?
R = 20 customers/hr, Rp = 0.429 /min or 25.71
U =R/Rp= 20/(25.71) = 77.7%
f) What is the average number of customers waiting in line?
Problem A5

## Slide 33: Problem A6: M/G/1 Example
A study-aid desk staffed by a graduate student has been established to answer students' questions and help in working problems in your SOM course. The desk is staffed 8 hours per day. The dean wants to know how the facility is working. Statistics show that students arrive at a rate of 8 per hour following Poisson distribution. Assistance time has an average of 6 Minutes and deviation of 3 minutes.
R= 8/hr
Rp = 60/6 = 10 /hr
OR
Rp = 1/6 per min or 60(1/6) = 10 /hr
U = 8/10 = 0.8

## Slide 34: Problem A6 : M/G/1 Example
1.What percentage of time the graduate student is idle? U = 0.8
80% of time the server is busy. 20% idle.
2. Calculate the average number of students in the waiting line.
Interarrival time follows exponential distribution  Ca =1
Processing time follows general distribution, Tp=6, Sp = 3
Cp = Sp/Tp = 3/6 = 0.5

## Slide 35: Problem A6: M/G/1 Example
3. Calculate the average number of students in the system.
Ip=Ii+Ip
Ip = cU = U = 0.8
Ii= 2
I =2+0.8 = 2.8
4. Calculate the average time in the system.
RT=I
8T = 2.8
T= 0.35 hr
T= 60(0.35) = 21 min