## Slide 1: Waiting Line Analysis
Ardavan Asef-Vaziri
These slides have been developed on the foundations provided by the following books.

## Slide 2: Article: The Psychology of Waiting Lines
Unoccupied time feels longer than occupied time.
Pre-process waits feels longer than in-process waits.
Anxiety makes waits seem longer.
Uncertain waits are longer than known, finite waits.
Unexplained waits are longer than explained waits.
Unfair waits are longer than equitable waits.
The more valuable the service, the longer I will wait.
Solo waiting feels longer than group waiting.

## Slide 3: Make to Stock (MTS) vs. Make to Order (MTO)
Made-to-stock (MTS) operations. Product is manufactured and stocked in advance. Safety inventory protects against stockouts due to variability of arrival time and processing time. Inventory also permits economies of scale.
  Make-to-order (MTO) operations. Each order is specific, cannot be stored in advance. Ex. banks, restaurants, retail checkout counters, airline reservation, hospitals , repair shops, call centres. Production systems also try to follow Dell Computer model. We needs to maintain sufficient capacity to deal with uncertainty in both arrival and processing time. Safety Capacity vs. Safety Inventory.

## Slide 4: Capacity More than Demand- Still Waiting Lines? Variability
The time of the arrival of an order is not known ahead of time. It is a random variable with estimated Ta (average) and Sa (standard deviation).
  The time of the next telephone call is not known.
  The time of arrival of the next car into a gas station is not known.
The service time is not known (precisely) ahead of time. It is a random variable with estimated Tp (average) and Sp (standard deviation).
  The time a customers spends on the web page of amazon.com is not precisely known.
  The time a customer spends speaking with the teller in the bank is unknown.

## Slide 5: AVERAGE Processing Time Tp & AVERAGE Processing Rate Rp
Tp : Activity processing time or Resource unit load. It is stated in terms of units of time. Ex. on average it takes 5 minutes to serve a customer, Tp=5.
Rp : processing rate. This many flow units are handled per unit of time.
What is the relationship between Tp and Rp?
Tp = 5 min, Rp =?
5 min 1 unit
1 min Rp How many units per minute?
Rp=(1×1)/5 =1/5 flow units per minute.

## Slide 6: AVERAGE Processing Time Tp & AVERAGE Processing Rate Rp
If Tp is 5 minutes, and there are three resource units, compute Rp for the resource pool.
Tp = 5 minutes. Processing time is 5 minute. Each customer on average is with the server for 5 minutes.
c = 3, we have three servers.
Processing rate of each server is 1/5 customers per minute, or 12 customer per hour.
Rp is the processing rate of all three servers.
Rp = c/Tp  Rp = 3/5 customers/minute, or 36 customers/hour.
For one resource unit, Rp =1/Tp
For c resource units c(1/Tp)= c/Tp

## Slide 7: Inter-arrival Time (Ta) and Arrival Rate (Ra)
Ta : customer inter-arrival time.
On average each 10 minutes one customer arrives.
Ra: customer arrival (inflow) rate.
What is the relationship between Ta and Ra?
Ta = every ten minutes one customer arrives
How many customers in a minute? Ra= 1/Ta= 1/10
Ra = 1/10 customers per min; 6 customers per hour  Ta= 1/Ra=1/6 hour.
Ra MUST ALWAYS <= Rp. We will show later that even Ra=Rp is not possible.
Incoming rate must be less than processing rate.
Throughput = Flow Rate R = Min (Ra, Rp) .
Stable Process = Ra< Rp  R = Ra
Utilization = inflow-rate/processing-rate = throughout/capacity = U = R/ Rp < 1
Safety Capacity = Rs = Rp – Ra

## Slide 8: The Relationship Between U and Ip
Given a single server, R = 6 per hour, processing time for a single server is 5 min  Rp= 12 per hour,
U = R/ Rp = 6/12 = 0.5  Rp – R = 12-6 = 6
How many flow units are in the server ?
U = 0.5 means 50% of time there is 1 flow unit in the server, 50% of time there is 0 flow unit in the server
0.5  1 + 0.5  0 = 0.5  Average Inventory in the server is equal to utilization
Ip= 1U = U
Given 2 servers, and a utilization of U = 0.3, How many flow units are in the servers ?
U = 0.3 means 30% of time there is 1 flow unit in each server, and 70% of time there is 0 flow unit in each server.
0.3  1 + 0.7  0 = 0.3 flow unit in each server
Average Inventory in the server is equal to utilization times the number of servers
Ip = cU =2(0.3) = 0.6 flow units with the servers.

## Slide 9: What We Have Learned Without Looking for any Formula
Processing time of a set of servers is Tp = 5 minutes. There are c=3 servers. Utilization of these servers is U=0.8.
Tp is also waiting time in the server, no mater one server or c servers. Tp in this example is always 5 min.
a) Compute the processing rate of this system. Rp=?
Processing rate Rp= c/Tp. Ex. Rp =3/5 per min; 36/hr
b) Compute the throughput.
U = R/Rp  0.8 =R/36  R=28.8 in our example
It worth to have the following insight too.
Ip= Tp  R (due to the Little's Law), and also Ip= cU, therefore R = cU/Tp
c) On average how many flow units are in these servers?
Ip = cU = 3(0.8) = 2.4, alternatively Ip= Tp  R =28.8(5/60) = 2.4.
d) What is the average interarival time between two consecutive customers ?
Ta = 60/28.8 =2.08 minute

## Slide 10: A Call Centre
Sales Reps
Processing
Calls
(Service Process)
Incoming Calls
(Customer Arrivals)
Calls
on Hold
(Service Inventory)
Answered Calls
(Customer Departures)
Blocked Calls
(Due to busy signal)
Abandoned Calls
(Due to long waits)
Calls In Process
(Due to long waits)
A Call Centre Process
Flow time T = Ti + Tp
Inventory I = Ii + Ip
Ti: waiting time in the inflow buffer.
Ii: number of customers in the inflow buffer.

## Slide 11: Characteristics of Waiting Lines
Variability in arrival time and service time leads to
  Idleness of resources
  Waiting time of flow units
We are interested in two measures
  Average waiting time of flow units in the waiting line and in the system (Waiting line + Processor).
  Average number of flow units waiting in the waiting line (to be then processed).
Let us first look at the Servers or Processors

## Slide 12: The Little’s Law Applies Everywhere
Flow time T = Ti + Tp
Inventory I = Ii + Ip
R
I = R T
R = I/T = Ii/Ti = Ip/Tp
Ii = R Ti
Ip = R  Tp
We know that U= R/Rp
We have already learned Rp = c/Tp, R= Ip/Tp
We can show U= R/Rp = (Ip/Tp)/(c/Tp) = Ip/c
But it is intuitively clear that U = Ip/c

## Slide 13: Operational Performance Measures
Flow time T = Ti + Tp
Inventory I = Ii + Ip
We know Tp and we can compute Ip at least in two ways.
Ti: waiting time in the inflow buffer = ?
Ii: number of customers waiting in the inflow buffer =?
Given our understanding of the Little’s Law, it is then enough to know either Ii or Ti.

## Slide 14: Utilization – Variability - Delay Curve
Variability
Increases
Average # of units in the system
Utilization
U
100%
Ip= SUM(cU)
Ip= R/ThFT
I

## Slide 15: Utilization and Variability
Our two measures of effectiveness (average number of flow units waiting and their average waiting time) are driven by
  Utilization (U-Part): The higher the utilization the longer the waiting line/time.
  Variability (V-Part): The higher the variability, the longer the waiting line/time.
High utilization U= R/Rp or low safety capacity Rs =Rp – R, due to
  High inflow rate R
  Low processing rate Rp = c/Tp, which may be due to small-scale c and/or slow speed 1/Tp
Variability in the interarrival time and processing time is measured using standard deviation. Higher standard deviation means greater variability.
Standard deviation is not enough to understand the extend of variability. Does a standard deviation of 20 represents more variability or a standard deviation of 150
for an average of 80
for an average of 1000?

## Slide 16: The Queue Length Approximation Formula
U= R /Rp, where Rp = c/Tp
Ca and Cp are the Coefficients of Variation
Standard Deviation/Mean of the inter-arrival or processing times (assumed independent)
Utilization effect
U-part
Variability effect
V-part

## Slide 17: Factors affecting Queue Length
Utilization effect; the queue length increases rapidly as U approaches 1.
Variability effect; the queue length increases as the variability in interarrival and processing times increases.
While the capacity is not fully utilized, since U must be less than 1, if there is variability in arrival or in processing times, queues will build up and customers will have to wait.

## Slide 18: Coefficient of Variations for Alternative Distributions
Tp: average processing time  Rp =c/Tp
Ta: average interarrival time  Ra = 1/Ta
Sp: Standard deviation of the processing time
Sa: Standard deviation of the interarrival time

## Slide 19: Coefficient of Variation
If processing time (Tp) or interarrival time (Ta) follow exponential distribution, then the corresponding CV is 1 (in exponential distribution standard deviation is equal to the average). Therefore, coefficient of variations for interarrival time (Ca) and/or processing time (Cp) is 1.
If both follow Exponential, then
Note that if we can remove variability, then Ii =0 and no one is waiting in a line even if U is very close to 1.
From now on, unless stated otherwise, we assume Ta and Tp follow exponential distribution and therefore R=Ram and both R & Rp follow Poisson process.

## Slide 20: Utilization and Safety Capacity
Interarrival time is 8 minutes. Processing time is 7.5 minutes. There is only one server.
Both interarrival time and processing time follow Exponential distribution.
How long a flow unit stays with the server?
Tp = 7.5 min
How many flow units are with the server?
Ra= 1/8 per minute or 60(1/8) = 7.5 per hr,
Rp = 1/7.5 per minute or 60(1/7.5) = 8 per hr
Ra< Rp  R=Ra  U= R/Rp
U = 7.5/8 = 0.9375
Ip-cU. Since there is only one server, Ip = 0.9375
How many flow units are in the waiting line?
= 14.0625
While U = 0.9375 <1 and safety capacity Rs = RP - Ra = 8 -7.5 = 0.5/hr, still On average 14.1 passengers waiting in line.

## Slide 21: Utilization and Safety Capacity
Waiting time in the line? RTi = Ii
Ti=Ii/R = 14.0625 /7.5 = 1.875 hr or 60(1.875)= 112.5 min.
Waiting time in the system?
T = Ti+Tp
Since Tp = 7.5  T = Ti+ Tp = 112.5+7.5 = 120 min.
Total number of passengers in the system?
I = RT = ( 7.5/60)(120) = 15
Alternatively, 14.0625 are in the buffer. How many are with the processor?
0.9375
I = 14.0625 + 0.9375 = 15
After few more computations, we will start using predesigned Excelsheets with Macros for these computations. But it is important to understand the quantitative relationships that we have discussed.

## Slide 22: Utilization and Safety Capacity
Total number of passengers in the system?
I = RT = ( 7.5/60)(120) = 15
Alternatively, 14.0625 are in the buffer. How many are with the processor?
0.9375
I = 14.0625 + 0.9375 = 15
Now suppose there are 2 processors, c=2
R is still 1/8 per minute or 7.5 per hour
Rp= 2/7.5 per minutes or 60(2/7.5) = 16 /hr
U = R/Rp = 7.5/16 = 0.46875
= 0.294222
On average Ii = 0.29 passengers waiting in line.

## Slide 23: Now suppose we have two servers
On average Ii = 0.29 passengers waiting in line.
Safety capacity is Rs = RP - R = 16-7.5 = 8.5 flow units per hour.
Ti=Ii/R = (0.294222/7.5)60 = 2.3538 min.
Total time in the system: T = Ti+Tp
Since Tp = 7.5  T = Ti + Tp = 7.5+2.4= 9.9 min
Total number of passengers in the process:
I = 2(0.4688) = 0.9376 in the buffer and 0.2942 in the process.
I = 0.94 + 0.29 = 1.23

## Slide 24: G/G/c
Consider a call center that employs 8 agents. Past data collected on the customer inter-arrival times has shown that the mean time between customer arrivals is 1 minute and has a standard deviation of 1/2 minute. The amount of time in minutes the past 10 callers have spent talking to an agent is as follows:
    4.1, 6.2, 5.5, 3.5, 3.2, 7.3, 8.4, 6.3, 2.6, 4.9.
  a) What is the coefficient of variation for the inter-arrival times?
  (standard deviation) / mean = 0.5/1 = 0.5
  b) What is the mean time a caller spends talking to an agent?
  = 5.2 minutes
  c) What is the standard deviation of the time a caller spends talking to an agent?
  = 1.88 minutes
d) What is the coefficient of variation for the times a caller spends talking to an agent?
  (standard deviation) / mean = 5.2/1.88 = 2.77
  (standard deviation) / mean = 1.88/5.2 = 0.192

## Slide 25
e) What is the expected number of callers on hold, waiting to talk to an agent?
R= 1 per minute, c = 8, processing rate for one agent is = 1/5.2. For c=8 agents, Rp = 8/5.2 = 1.54 /min
U = R/Rp= 1/(1.54) = 0.65
G/G/c
f) What is the expected number of callers either on hold or talking to an agent?
I = Ii + Ip= 0.09 + 0.65(8) =5.29
g) What is the expected amount of time a caller must wait to talk to an agent?
RTi = Ii  Ti = 0.09/1 = 0.09 minutes

## Slide 26
G/G/c
h) What is the expected amount of time between when a caller first arrives to the system, and when that caller finishes talking to an agent?
T = I/R = 5.29/1 = 5.29 minutes
Alternatively; T= Ti+Tp = 0.09+5.2 = 5.29

## Slide 27: Terminology and Classification of Waiting Lines
Terminology: The characteristics of a waiting line is captured by five parameters; arrival pattern, service pattern, number of server, queue capacity, and queue discipline. a/b/c/d/e
M/M/1; Poisson arrival rate, Exponential service times, one server, no capacity limit.
M/G/12/23; Poisson arrival rate, General service times, 12 servers, queue capacity is 23.
Approximation formula gives exact answers for M/M/1 system.
Approximation formula provide good approximations for M/M/2 system.
From Now on, for all computations Regarding M/M/c (including M/M/1), M/G/1 (including M/D/1) and M/M/c/b we use predesigned Excelsheets with Macros.
For other situations, we use the approximation formula.

## Slide 28: Ta = 8 mins. Tp = 7.5 mins. C=1

## Slide 29: Ta = 8 mins. Tp = 7.5 mins. C=2

## Slide 30
The arrival rate to a store is 6 customers per hour and follows Poisson distribution. The service time is 5 min per customer and follows exponential distribution.
a) Compute Processing time (How long does a customer stay with the cashier?)
Tp = 5 min.
b) On average how many customers are with cashier?
R= 6/ hr
Rp=1/Tp = 1/5 per min. or 60(1/5) = 12/hr
U= 6/12 = 0.5  Ip = 0.5
Alternatively;
RTp = Ip =
6(5/60) = 0.5
=(6/60)5 = 0.5
c) Compute Ii, Ti, Ip, Tp, I, and T.
d) What if arrival Rate changes to 11, 11.1, 11.2, ………11.9.

## Slide 31: Problem 1: M/M/1 Performance Evaluation
Average utilization rate of server - U | 50.0%
Average number of customers waiting in line Ii | 0.500
Average number of customers in system I | 1.000
Average time waiting in line Ti | 0.083
Average time in system - T | 0.167
 | 6 | 11 | 11.1 | 11.2 | 11.3 | 11.4 | 11.5 | 11.6 | 11.7 | 11.8 | 11.9
50.0% | 0.500 | 0.917 | 0.925 | 0.933 | 0.942 | 0.950 | 0.958 | 0.967 | 0.975 | 0.983 | 0.992
50.0% | 0.500 | 10.083 | 11.408 | 13.067 | 15.201 | 18.050 | 22.042 | 28.033 | 38.025 | 58.017 | 118.01
100.0% | 1.000 | 11.000 | 12.333 | 14.000 | 16.143 | 19.000 | 23.000 | 29.000 | 39.000 | 59.000 | 119.00
8.3% | 0.083 | 0.917 | 1.028 | 1.167 | 1.345 | 1.583 | 1.917 | 2.417 | 3.250 | 4.917 | 9.917
16.7% | 0.167 | 1.000 | 1.111 | 1.250 | 1.429 | 1.667 | 2.000 | 2.500 | 3.333 | 5.000 | 10.000

## Slide 32: Problem 1: M/M/1 Performance Evaluation
R= 6/hour with Poisson distribution. Tp = 5 min with exponential distribution.
U
V
Ii

## Slide 33: Problem 2: M/M/1 Performance Evaluation
Case 1. An airport runway for arrivals only. Arriving aircraft join a single line for the runway. Exponentially distributed service time with a rate 25 arrivals /hour. Poisson arrivals with a rate 18 / hour. Compute Tp, Ip, Ii, Ti, I, and T. Case 2. Now suppose we are in holidays and the arrival rate increases to 21 arrivals/hour. Case 3. Now suppose we have a bad weather, and the service rate decreases 22 landing /hour. Case 4. Now suppose we open a second runway. R=21, Rp=2*25/hr  U= 21/50 = 0.42

## Slide 34
Bank of San Pedro has only 1 teller. On average, 1 customer comes every 6 minutes, and it takes the teller an average of 3 minutes to serve a customer. To improve customer satisfaction, the bank is going to implement a unique policy called, “We Pay While You Wait.” Once implemented, the bank will pay each customer $3 per minute while a customer waits in line. (So the clock starts when a customer joins the line and stops when the customer begins to talk to the teller.) Bank of San Pedro hired you as a consultant and you are responsible for estimating how much the “We Pay While You Wait” program will cost. Assume linear cost. If a customer waits for ten seconds in line, Bank of San Pedro will pay $0.5. Assume that arrival follows Poisson and service time follows exponential distribution.
Compute the capacity of the Teller Station.
It takes the teller an average of 3 mins to serve a customer, 60/3 = 20 customers per hr.
b) Compute the proportion of the time the teller is busy.
R=10, Rp= 20  U= R/Rp= 10/20 = 0.5  Busy 50%, Idle 50%.
c) Compute key waiting line Metrics.
Problem 7

## Slide 35
Average utilization rate of server - U
Average number of customers waiting in line Ii
Average number of customers in system I
Average time waiting in line Ti
Average time in system - T
Ii= 0.5
There is 0.5 customers around the clock in the waiting line.
We pay $3 per minute for one customer in the line. That is $3(60) =$180 per hour for one customer in the line.
We have 0.5 customers, that is 0.5($180) = $90 per hour.
It seems you do not believe me.
Lets compute it in an alternative way.
Problem 7

## Slide 36
Average utilization rate of server - U
Average number of customers waiting in line Ii
Average number of customers in system I
Average time waiting in line Ti
Average time in system - T
Each customer spends 0.05 hours.
Why hour?
Because R and Rp were in hours. 0.5(60)= 3 minutes in the line.
He or she receives, on average, 3(3) =$9.
There are 10 customers arriving per hour.
The overall hourly cost of this program is 9*10=$90.
Problem 7

## Slide 37
e) Suppose each additional clerk costs X dollars per hour (including all other clerk related costs such as benefits, space and equipment hourly costs). Compute the maximum value of X if it is at our benefit to hire one additional clerk?
If we have two clerks, Rp increases from 20 to 40, and utilization drops from 0.5 to 10/40 = 0.25.
Ii= 0.0333 for two clerks.
Ii reduced from 0.5 customers to 0.033 customers = 0.467 reduction in the number of customers in the line.
That is 0.467(3(60))= $84 cost reduction.
We are ready to pay up to $84 for the second clerk.
f) Suppose each additional clerk costs $30 per hour. How many new clerk should we hire, one or two?
Obviously, it is at our benefit to hire one clerk. But lets also think about two.
Problem 7

## Slide 38
If we hire two clerks (to have 3 clerks), Rp increases to 60, and utilization drops 10/60 = 0.167. With three clerks, Ii os reduced to 0.003.
That is from 0.033 with two clerks to 0.003. That is 0.03 reduction.
By adding the third clerk, there are 0.03 less customers waiting in line (each hour and always)
180(0.03) = about $5-$6.
It is not at our benefit to hire the second additional clerk, pay $30 per hour capacity cost to reduce waiting cost by $5-$6 per hour.
We did not need to do this much computations for the third clerk. With two clerks the total number of customers waiting in line was 0.033.
Even if we reduce the number of customers in the waiting line to 0, we have reduced the line by 0.033(180) =$6. It is not worth the cost $30 to benefit $6
And we will pay not even one dollar (0.003(180)) for the fourth clerk.
Problem 7

## Slide 39
Server 1
Queue1
Server 2
Server 1
Queue
Server 2
20/hr
R
R
Problem 8. Effect of Pooling- M/M/2 vs. 2M/M/1
2M/M/1
M/M/2
Tp
Queue2
Tp

## Slide 40
Server 1
Queue1
Server 2
Server 1
Queue
Server 2
20/hr
10/hr
10/hr
Problem 8. Effect of Pooling- M/M/2 vs. 2M/M/1
2M/M/1
M/M/2
5 min
5 min
Queue2

## Slide 41
Problem 8. Effect of Pooling- M/M/2 vs. 2M/M/1

## Slide 42
Problem 8. Effect of Pooling- M/M/2 vs. 2M/M/1
Server 1
Queue1
10/hr
Tp= 5 min
U = R/Rp =10/12 = 5/6 
Ip = cU = U = 0.833 or
RTp =Ip  10(5/60) = 0.833
Tp= 5 min
Ip= 0.833
Server 2
10/hr
Queue2
Tp= 5 min
Ip= 0.833
Ip=
0.833
+0.833
---------
1.667
Ii = 4.167
Ii = 4.167
Ii = 2*4.167 = 8. 334
Ti = 25 min.
Ti = 25 min.
Ti = 25 min.
T= Tp+Ti = 5+ 25 = 30 mins

## Slide 43
Problem 8. Effect of Pooling- M/M/2 vs. 2M/M/1
Server 1
Queue
20/hr
Tp= 5 min
U = R/Rp =20/24 = 5/6 
Ip = cU = 2(0.833) = 1.667 or
RTp =Ip  20(5/60) = 1.667
Server 2
Ii = 3.79
Ti = 11.36 min.
T= Tp+Ti = 5+11.365 = 16.36 mins
Why is Design B better than A?
  Design A the waiting time of customer is dependent on the processing time of those ahead in the queue
  Design B, the waiting time of customer is only partially dependent on each preceding customer’s processing time
  Combining queues reduces variability and leads to reduce waiting times

## Slide 44
American Vending Inc. (AVI) supplies vending food to a large university. Because students often kick the machines out of anger and frustration, management has a constant repair problem. The machines break down on an average of 3/hr, and the breakdowns are distributed in a Poisson manner. Downtime costs the company $25/hr/machine, and each maintenance worker gets $4 per hr.
One worker can service machines at an average rate of 5/hr, distributed exponentially;
2 workers working together can service 7/hr, distributed exponentially;
and a team of 3 workers can do 8/hr, distributed exponentially. What is the optimal maintenance crew size for servicing the machines?
Problem 11

## Slide 45: Problem 11
c=????
c = 1
U=??
Down time cost = 25Ii
Capacity Cost= 4(# of team members)
Total Cost
Have I made any mistakes?
Downtime costs the company $25 /hr/machine.
When the machine is down?
Until it is up.
In the waiting line it is down. In the processor until the end of the process it is down.
There fore, besides Ii, I also need Ip
Ip is simply U+Ii

## Slide 46
Problem 11

## Slide 47
Lets check by using Ti and Tp instead of Ii and Ip
Problem 11

## Slide 48: Performance Improvement Levers
These slides have been developed on the foundations provided by the following book.

## Slide 49: Lessons Learned
If inter-arrival and processing times are constant, queues will build up if and only if the arrival rate is greater than the processing rate.
If there is (unsynchronized) variability in inter-arrival and/or processing times, queues will build up even if the average arrival rate is less than the average processing rate.
If variability in interarrival and processing times can be synchronized (correlated), queues and waiting times will be reduced.

## Slide 50: Performance Measures
Financial Performance Measures
  Sales: Throughput Rate
  Cost: Capacity utilization, Flow units in queue / in system
  Customer service: Waiting Time in queue /in system
Performance Improvement Levers
  Decrease variability in inter-arrival and processing times.
  Decrease capacity utilization.
  Synchronize available capacity with demand.

## Slide 51: 1. Arrival Variability Reduction Levers
Customers arrival are hard to control
  Better scheduling, Reservations, Appointments, Price differentials (matinee shows, early-bird , off-season rates for hotels) , alternative services (ATM, Online). Batch size reduction, JIT. etc…Demand management strategies. The objective is to reduce the arrival rate during peak periods of congestion as well as to reduce variability in inflows. If queues are visible to arrivals, demand management may be self-enforcing. Restaurant being so crowded that nobody goes there anymore!
Limit product variety, increase commonality of parts.

## Slide 52: 2. Capacity Utilization and Variability Reduction Levers
U↓ (or increase Rs)  delays ↓ and queues ↓. To decrease U = Ra/Rp or Rs=Rp-Ra), we can decrease capacity utilization (or increase safety capacity).
Increase scale of the process (c).
Increase speed of the process (Tp). Tp reduction: Methods, Training, Standardization, Technology, Lower employee turnover rate, More experienced work force, Parallel Processing, Pre-processing, Alternative Services. State of the art order processing at McDonald’s drive-through. Starbuck’s baristas often make multiple coffee drinks in parallel . Preregistration at hospitals or printing boarding passes online), Customer participation in a self-service salad bar.
Pool capacity across homogeneous arrivals and separate heterogeneous arrivals

## Slide 53: 3. Synchronizing Capacity with Demand
Capacity Adjustment Strategies
  Personnel shifts, cross training, flexible resources.
  Workforce planning & season variability.
  Synchronize the available processing capacity with demand, Better scheduling.

## Slide 54: Variability Reduction Levers - Arrivals
The average queue length (and hence waiting time in queue) is directly proportional to the sum of the squares of the two coefficients of variation of interarrival and processing times.
In manufacturing, reliable suppliers, (lover variability in lead time leads to reduced safety inventory), batch size reduction (leads to reduction of average inventories and flow times).
In service operations where there is only limited control over customer arrivals, it is possible to make arrivals more predictable through scheduling, reservations, and appointments. Medical offices and restaurants try to match capacity with uncertain demand through appointments and reservations. – there are still late arrivals and no show-ups.

## Slide 55: Variability Reduction Levers - Processing Times
To reduce variability in processing times, we must understand its source. A common resource may be used for producing a variety of products, each requiring very different processing times. We can reduce the processing time variability by limiting product variety or specializing resources to perform only a narrow range of processing. Standard express meal packs in fast food restaurants, specialized teller windows at banks, and separate extensions for different types of telephone calls. Processing times may be variable because of a lack of standardization or training . Toyota defines an exact sequence of activities for each workstation, resulting in a reduction in the variability in processing times as well as in the average processing time. Experienced workers tend not only to process faster but also do so with higher consistency in terms of the processing time (as well as output quality).

## Slide 56: Variability Reduction Levers - Processing Times
Therefore, any managerial actions and incentives aimed at maintaining a stable workforce and low turnover rate will lead to shorter and more consistent processing times and better process performance in terms of shorter queues and delays.
It is impossible to eliminate all sources of variability. Banks cannot force customers to come in at regular intervals; each customer decides when to go to the bank independently . Banks cannot eliminate processing time variability completely because different customers have different transaction needs, and all these cannot be standardized. In fact, the primary virtue of make-to-order processes is their ability to provide customization. Given the presence of unavoidable variability in inflow and processing times, managers must deal with it by investing in some safety capacity albeit at a higher cost.

## Slide 57: Capacity Synchronization Levers – Short Term
Synchronization of supply and demand requires managing either the supply (capacity) or the demand (arrival rates).
Adjusting capacity in response to demand may not be economical or even feasible . Examples are the number of rooms in a hotel or tables in a restaurant . We must manage demand; using off‑season hotel rates and differential pricing.
In the short term, adjusting human resources is easier than capital resources. Checkout counters are opened/closed depending on the number of waiting customers. This strategy also illustrates the advantages of pooling the available total capacity, but it requires that all personnel are trained to perform different tasks. Importance of resource flexibility in reducing the permanent capacity requirements.
Servers often tend to work faster as the queues get longer.

## Slide 58: Capacity Synchronization Levers – Long Term
In a somewhat longer time frame, synchronization is easier. In call centers and fast food restaurants—demand varies by the time of the day and the day of the week. This seasonality can be anticipated with a high degree of accuracy. The managers can then plan the required capacity (personnel) to match the forecasted demand. McDonald’s plans the required number of personnel in 15‑minute intervals by scheduling their shifts and breaks and by using part-time workers.
In manufacturing operations, managers can synchronize the arrival and processing rates by limiting the size of the buffer that is allowed to build up between the two workstations. The feeder workstation is then forced to stop once its output buffer is full. The synchronization decreases the in-process inventory and waiting time but also results in some loss of throughput.

## Slide 59: Pooling and Segregation Levers
8.8.5 Pooling and Segregation Levers
As we saw in Section 8.7, merging of queues of similar customers leads to improved utilization of the available capacity. Pooling is often implemented in banks, post offices, departments of motor vehicles, where a single line feeds into the server pool, instead of a separate line for each server. Similarly, in call centers, all customers call one number and are then routed to the next available agent. Note that if arrivals can see and switch between queues, then having separate queues for different servers is equivalent to a single queue that is served by the entire pool. Thus, for example, in restaurants such as McDonald’s, each cash register has a separate queue of customers waiting to place orders. However, if a server becomes idle, he/she takes orders from customers in adjacent lines (although perhaps not necessarily in the FCFS fashion).

## Slide 60: Pooling and Segregation Levers
Note, however, that pooling different types of customers increases variability in processing times and requires that the servers have sufficient flexibility to be able to process a variety of jobs. The cost of cross-training required must be weighed against the benefits of pooling. Similarly, we have seen above that specialization reduces the average processing time as well as its variability and may improve the service quality. Therefore, segregating customers according to their processing requirements will result in reduced waiting times and queues within each class. Supermarkets keep special checkout counters for customers with fewer items, which reduces the mean as well as variability in their processing times, thus reducing the average overall wait.
The key to allocating the available capacity is to collect information about processing requirements of customer arrivals, so that customers can be classified into homogeneous classes and each class can assigned to a separate pools of servers. The result will be reduced average and variability in processing times within each class due to server specialization.

## Slide 61: Managing Customer Perceptions and Expectations
Waiting has significant economic and behavioral implications.
Provide Comfort. Comfortable seating, well decorated surroundings, friendly staff.
Provide Distraction. TV monitors, video games, mirrors, etc.
Provide Information. Customers tolerate waits better if they are informed of the expected waiting times.
Provide Explanation. It creates the empathy if customers sense that the management is aware of the customers waiting and is doing something about it.
Manage Expectations. Customers are often willing to wait longer if the service itself is time consuming. Customers with full carts are willing to wait longer. Sometimes, pessimistic estimates are provided so customers are pleasantly surprised when the actual wait turns is less than the announced period.

## Slide 62: Managing Customer Perceptions and Expectations
Ensure Fairness Customers complain if later arrivals have been served first. Pooling arrivals in a single waiting line creates a sense of fairness; with separate waiting lines, the other line always seems to move faster than ours! Although providing priority service to customers paying a premium price may be economically rational, it may appear unfair to the rest who perceive that the rich get preferential treatment.
Sometimes quick service and short waits may be perceived to imply lower quality experience! Fine dining experience would involve a long, leisurely meal, prepared and served in a relaxed atmosphere.
Managing customer expectations and perceptions of the wait could be just as important a lever as reducing the actual waiting time itself.

## Slide 63
Bank of San Pedro has only 1 teller. On average, 1 customer comes every 6 minutes, and it takes the teller an average of 3 minutes to serve a customer. To improve customer satisfaction, the bank is going to implement a unique policy called, “We Pay While You Wait.” Once implemented, the bank will pay each customer $3 per minute while a customer waits in line. (So the clock starts when a customer joins the line, and stops when the customer begins to talk to the teller.) Bank of San Pedro hired you as a consultant and you are responsible for estimating how much the “We Pay While You Wait” program will cost. Your preliminary study indicates there are, on average, 0.5 customers waiting in line. Assume linear cost. If a customer waits for ten seconds in line, Bank of San Pedro will pay $0.5. Assume that arrival follows Poisson and service time follows exponential distribution.
Problem 12

## Slide 65
$130 (3) = 390